## Slide 1: Firmware 102

## Slide 2: Overview
Installing software
Why not Arduino?
Tips for success
First steps
Taking it further
firmware 102

## Slide 3: Installing software
Atmel Studio 7 - https://www.microchip.com/avr-support/atmel-studio-7
It’s gonna take a while and need a reboot, so get to it. Expect about 15 minutes.
Install for AVR 8-bit MCU
Stick avrdude.* somewhere simple like C:\
firmware 102

## Slide 4: Why not Arduino?
firmware 102
Arduino is a great starting place
It abstracts all the nitty-gritty so it can support lots of MCUs
The IDE is super simple
Don’t need to think about multiple files or file management

## Slide 5: Why not Arduino?
firmware 102
Arduino is a great starting place
It abstracts all the nitty-gritty so it can support lots of MCUs
- and as such, you don’t learn about the finer points of your processor
The IDE is super simple
- so simple that you’re going to go mad trying to do much more than ‘hello world’
Don’t need to think about multiple files or file management
- everyone loves a 5000 line source file, right?

## Slide 6: So what then?
firmware 102
Notepad?
Atmel Studio?

## Slide 7: avr-libc
firmware 102
Open source binutils and libc for the AVR processors
binutils
Utilities for converting assembly code to binary
ld – program linker
as – assembler
objcopy, strip, ar, etc..
gcc
The GNU compiler
libc
The standard C library
stdio, stderr
printf, malloc, etc

## Slide 8: avr-libc – avrdude
firmware 102
AVRDUDE
AVR Downloader/UploaDEr
Handles programming your AVR
Read/Write flash, fuses, eeprom
Multiple bootloaders/programmers supported
Part of avr-libc
Included with Arduino, but not Atmel Studio
- So I grabbed it for you

## Slide 9: Tips for success
firmware 102
Know your circuit schematic
Keep the datasheet handy
Code and debug one thing at a time
Use comments and verbose code

## Slide 10: Hardware
firmware 102

## Slide 11: The Schematic – Arduino Uno
firmware 102

## Slide 12: The Schematic – Arduino Uno – Break it down
firmware 102
USB Interface
Power Supply
Power Select
Blinker
MCU
IO
Clock

## Slide 13: The Schematic – DC801 Shield
firmware 102

## Slide 14: The Schematic – DC801 Shield – Break it down
firmware 102
Shield IO
Blinkies
Buttons

## Slide 15: The Schematic - Simplfy it
firmware 102

## Slide 16: The Schematic – The imporant bits
firmware 102
Port B
Port D

## Slide 17: Setting up your Uno
firmware 102
If Windows doesn’t install the driver for your board, use the drivers I gave you
If you have a fresh Uno, it should blink an LED when you plug it into the USB
For Step 1, leave the shield off

## Slide 18: Configuring Atmel Studio
firmware 102
Tools -> External Tools…
Arguments:
-C"C:\avrdude.conf" -patmega328p -carduino
-PCOM3 -b115200 -D
-Uflash:w:"$(ProjectDir)Debug\$(TargetName).hex":i
COM port might be different, check with device manager

## Slide 19: Step 1 – Blink!
firmware 102
Step1 project

## Slide 20: Software first steps
Build -> Build Solution (or press F7)
Make sure your Uno is plugged in
Tools -> avrdude
Blink!
firmware 102

## Slide 21: Under the hood
firmware 102
When you hit build
gcc compiles your code into assembly
as converts the assembly into object code
ld links the object code and figures out actual program offsets
objcopy converts the output to a hex file
avrdude flashes the chip

## Slide 22: Port B? Data direction registers?
firmware 102

## Slide 23: Waiting?
firmware 102
_delay_ms does a busy wait – based on CPU frequency, it executes a bunch of NOPs

## Slide 24: Bit shifting??
firmware 102
Set low –
Read the current port pins
(1 << 5) - Shift a 1 5 bits = 0001 0000
~ - bitwise invert it = 1110 1111
Bitwise AND the two – anything not set will be set low
Set the port
Set high –
Read the current port pins
(1 << 5) - Shift a 1 5 bits = 0001 0000
Bitwise OR the two – anything with a 1 will be set high
Set the port

## Slide 25: #define is your friend
firmware 102
Pre-processor defines can transform
into
and save your sanity

## Slide 26: Step 2 – Putting it together
firmware 102
Step2 project

## Slide 27: Step 3 – Putting it together – Now with more files
firmware 102
Step3 project
Defines and routines not cluttering up our source!

## Slide 28: Step 4 – More blinkies
firmware 102
Step4 project

## Slide 29: Step 5 – Input – Pullups
firmware 102
To read a pin, it needs to solidly be either low (0V) or high (5v)
A pullup resistor forces the signal to high when the switch is not pressed
Most atmega MCUs can be configured to use an internal pullup

## Slide 30: Step 5 – Input
firmware 102
Step5 project

## Slide 31: Step 5 – Input – Problems
firmware 102
Some problems with our input example
Button is not read until after the LED is blinked
Button is not debounced

## Slide 32: Step 6 – Input – Debounce
firmware 102
Software debounce: read the state, wait, and read again usually covers the bounce

## Slide 33: Wrap up
firmware 102
That’s the basics – play with the code, figure out how to make the eyes light up
Next time around we’ll figure out interrupts and PWM

## Slide 34
Questions?
Snide Comments?
@hamster
firmware 102